## Slide 1: Digital Low Pass Filter
Tom Zimmerman
IBM Research-Almaden
4.18.23
This material is based upon work supported by the NSF under Grant No. DBI-1548297.
Disclaimer: Any opinions, findings and conclusions or recommendations expressed in this material are those of the authors and do not necessarily reflect the views of the National Science Foundation.

## Slide 2
A
B
C
Amplitude
Frequency
Represent Signal in Time and Frequency Domain
Any Waveform Synthesized from Sum of Sine Waves
Types of Filters
Low Pass Filtering of Noisy (High Frequency) Data
Cutoff Frequency of Low Pass Filter
LOG UNITS
octave=2*frequency
6dB=2*amplitude
-6dB=0.5*amplitude
amp=1/n (1, 1/3, 1/5...)
odd harmonics
(1,3,5,... x fundamental freq)

## Slide 3
Sout = fc * Sout + (1- fc)Sin
fc = 0.0 to 1.0
Larger fc value means lower cutoff frequency i.e., less noise but more lag. Suggestions: Start with 0.9. Initialize Sout=Sin
One-Pole (-3dB/octave) Digital Low Pass Filter
fc =
fc =0.9
fc =0.8
fc =0.95

## Slide 4
import numpy as np
import matplotlib.pyplot as plt
MAX_SAMPLES=100
f1=0.8
f2=0.9
f3=0.95
s=np.zeros(MAX_SAMPLES)
S1=np.zeros(MAX_SAMPLES)
S2=np.zeros(MAX_SAMPLES)
S3=np.zeros(MAX_SAMPLES)
s[int(MAX_SAMPLES/2):MAX_SAMPLES]=1
S1[0]=s[0] # bootstrap output with first sample
S2[0]=s[0] # bootstrap output with first sample
S3[0]=s[0] # bootstrap output with first sample
for i in range(1,MAX_SAMPLES-1):
S1[i+1] = f1*S1[i] + (1-f1)*s[i]
S2[i+1] = f2*S2[i] + (1-f2)*s[i]
S3[i+1] = f3*S3[i] + (1-f3)*s[i]
plt.plot(S1)
plt.plot(S2)
plt.plot(S3)
plt.plot(s)