## Slide 1
This material is based upon work supported by the NSF under Grant No. DBI-1548297.
Disclaimer: Any opinions, findings and conclusions or recommendations expressed in this material are those of the authors and do not necessarily reflect the views of the National Science Foundation.
Slide Holder Design
Tom Zimmerman
IBM Research-Almaden
Center for Cellular Construction
3.3.21

## Slide 2
Magnification
M=L/z
Image Sensor
Laser
Slide w/ Specimen
z
L
Objectives: Make a simple 3D printed slide holder that (1) allows variable magnification by selecting the distance between the slide and laser (Z) and (2) allows the manual x and y movement of the slide relative to the image sensor and laser to select objects of interest on the slide.

## Slide 3
Standard Glass Slide
75 mm x 25 mm x 1 mm
L=
25 mm
Slot Opening Size: 40mm wide x 2mm high
Equally space them vertically and centered. Same slots on the opposite sides so a slide can pass through in x direction. The 40 mm width allows slide to move in y direction. The four slots allow selection of laser-to-specimen (Z), while the laser-to-image sensor (L) is fixed.
y=50 mm
x=50 mm
Slide Holding Cap for Holographic Microscope