## Slide 1: Detection, Tracking and Identification Microscope Projects
Tom Zimmerman
IBM Research-Almaden
Sept 10, 2019
This material is based upon work supported by the NSF under Grant No. DBI-1548297.
Disclaimer: Any opinions, findings and conclusions or recommendations expressed in this material are those of the authors and do not necessarily reflect the views of the National Science Foundation.

## Slide 2
Raw (color)
Detection
(Raw – Background)
(grey & threshold)
Tracking
(contours)
Background
(Median Filter)

## Slide 3
Simple Background Estimation in Videos using OpenCV by Satya Mallick
https://www.learnopencv.com/simple-background-estimation-in-videos-using-opencv-c-python/

## Slide 4
def createBackgroundImage(vid):
maxFrame=10000
# Open Video
print ('openVideo:',vid)
cap = cv2.VideoCapture(vid)
# Randomly select 25 frames
print('calculating median')
frameIds = maxFrame * np.random.uniform(size=25)
# Store selected frames in an array
frames = []
for fid in frameIds:
cap.set(cv2.CAP_PROP_POS_FRAMES, fid)
ret, frame = cap.read()
frames.append(frame)
# Calculate the median along the time axis
medianFrame = np.median(frames, axis=0).astype(dtype=np.uint8)
# Convert background to grayscale
grayMedianFrame = cv2.cvtColor(medianFrame, cv2.COLOR_BGR2GRAY)
# Display median frame
print('display background frame')
cv2.imshow('background', cv2.resize(grayMedianFrame,(xRez,yRez)))
cap.release()
return(grayMedianFrame)

## Slide 5
def processVideo(vid,outFileName,grayMedianFrame):
cap = cv2.VideoCapture(vid)
frameCount=0
while(cap.isOpened()):
ret, rawIM = cap.read()
if not ret: # check to make sure there was a frame to read
print('no more frames to read')
break
grayIM = cv2.cvtColor(rawIM, cv2.COLOR_BGR2GRAY)
diffIM = cv2.absdiff(grayIM, grayMedianFrame)
th, threshIM = cv2.threshold(diffIM, thresh, 255, cv2.THRESH_BINARY)
# get contours
im2,cnt, hierarchy = cv2.findContours(threshIM, cv2.RETR_EXTERNAL, cv2.CHAIN_APPROX_NONE)
objCount=0
for c in cnt:
area = int(cv2.contourArea(c)) #COMPUTING AREA
if area>minArea and area<maxArea: #LET'S CHOOSE THE AREA THAT WE WANT
  PO = cv2.boundingRect(c)
  x0=PO[0]; y0=PO[1]; x1=x0+PO[2]; y1=y0+PO[3]
  xc=x0+(x1-x0)/2; yc=y0+(y1-y0)/2
  boundArea=(y1-y0)*(x1-x0)
  pixOn=np.sum(threshIM[y0:y1,x0:x1])/255
  cv2.rectangle(rawIM, (x0,y0), (x1,y1), (255,0,0), 3)
  objCount+=1
cv2.imshow('track', cv2.resize(rawIM,(xRez,yRez))) #display object
cv2.imshow('thresh', cv2.resize(threshIM,(xRez,yRez))) #display object
print('done')
cap.release()
cv2.destroyAllWindows()
return

## Slide 6
Image Processing with Python and OpenCV
Detection
  Thresholding (select bright or dim objects from image)
  Template matching (convolution of image with template)
  Background subtraction (detect moving objects)
Tracking
  Contour library function (OpenCV)
  Cam (Tom Z method)
Identification
  Find nearest neighbor

## Slide 7
HARDWARE PROJECTS
Optics
Magnification; change distance between object and image sensor
measure resolution and field of view
Web camera as holographic microscope
Lighting
Blue Laser for higher resolution
White LED for color image
Pin hole; Use to increase fringes and holographic resolution
Make pinhole by electric discharge, chemical, mechanical (pin, multi-layer aluminum or brass)
Multiple light source; laser, LED, combination, to increase sensing area
Stereo imaging; simultaneous or frame sequential
Sample
Move sample stage with servo motor or stepper motor
Pump to feed samples from tubes
Packaging
Waterproof submersible microscope
Cool sensor so it doesn’t cook samples; heat sink, water, Peltier cooler
Battery powered

## Slide 8
SOFTWARE PROJECTS
Holographic reconstruction
Auto-track Z based on image sharpness, edge, contrast
Heuristics (where plankton was in last frame)
Stereo using two light sources (LED and laser)
  Z stack creating, modeling, presentation
  Knobs (potentiometers) for interactive reconstruction
Classification
Feature extraction
Unsupervised classification
Machine learning classification (SVM, Random Forrest)
Explore exposure and other image sensor settings
Enhanced Imaging
High resolution imaging using full 5 Mpix (still images)
Super-resolution by small movements of image sensor or light source (e.g. RGB LED)
Detect, Track, ID
Detection, tracking, identification; improve speed & accuracy performance

## Slide 9
BIOLOGY PROJECTS
Samples
Collect samples from outside and classify
Spatial and temporal distribution sampling and modeling
Chemical Response
Chemical impact on plankton shape and movement, short term and long term
Thermal impact (hot or cold)
Inter-species Interaction
Predator/pray, symbiotic
Long Term Monitoring
Observe life cycle (reproduction)