## Slide 1: Holographic Microscope Optimal Configuration
Tom Zimmerman
IBM Research-Almaden
Feb 18, 2021
This material is based upon work supported by the NSF under Grant No. DBI-1548297.
Disclaimer: Any opinions, findings and conclusions or recommendations expressed in this material are those of the authors and do not necessarily reflect the views of the National Science Foundation.

## Slide 2
DIHM_Camera_V3.py

## Slide 3
Magnification
M=L/z
Open-source, cost-effective, portable, 3D-printed digital lensless holographic microscope
Heberley Tobon-Maya, Samuel Zapata-Valencia, Erick Zora-Guzman, Carlos Buitrago-Duque, AND Jorge Garcia-Sucerquia*
School of Physics, Universidad Nacional de Colombia—Sede Medellin, A.A: 3840, Medellin 050034, Colombia

## Slide 4
Two Operating Regimes
Gabor’s like implementation. Sample close to point source. The sample’s diffraction pattern is magnified (geometric projection) 5X to 20X (similar to optical microscope), ∼0.4–0.5NA
Lensless Holographic Microscopy (LHM) Sample close to image sensor. No geometric magnification. Resolution limit by detector, not diffraction. FOV becomes whole detector. ∼0.2 NA range. Super-resolution can be used to decrease effective pixel size.
Common Problems
Coherent Noise; use partially coherent sources, overlapping several in-line holographic images
Weak Diffraction Assumption; prevents image formation in Gabor, restricts range of samples in LHM; applying special implementations of phase-shifting holography
Twin image problem: direct consequence of the in-line configuration. Avoided in LHM by using two different strategies: phase-shifting and phase retrieval algorithms. Phase shifting: relative phase variation between interferometric beams. Phase retrieval: iterative or deterministic algorithms. Record several images in time at multi-height with glass cover slips of different thicknesses, move camera, tune the light wavelength or defocus the image.

## Slide 5
22 mm
0.5 mm
7 mm
Tri Color Laser: CD (IR-780nm), DVD (red-660nm) Blue-ray (blue-405nm)
MISHELF (initials coming from Multi-Illumination Single-Holographic-Exposure Lensless Fresnel)
commercial-grade plastic lens of 0.6NA.

## Slide 6
Open-source, cost-effective, portable, 3D-printed digital lensless holographic microscope
Heberley Tobon-Maya, Samuel Zapata-Valencia, Erick Zora-Guzman, Carlos Buitrago-Duque, Jorge Garcia-Sucerquia
School of Physics, Universidad Nacional de Colombia—Sede Medellin, A.A: 3840, Medellin 050034, Colombia
FOV 0.023 to 10mm spatial resolution 1.15 to 6.3um

## Slide 7
Calculations based on “3D-printable portable open-source platform for low-cost lens-less holographic cellular imaging” by
Stephan Amann , Max von Witzleben & Stefan Breuer
Their system:
p=1.12 um, N=2464, f=30 mm, L (lamda)=405, 430
SYSTEM | pix rez | N pix | Light:Detect (um) | Wavelength (um) | Obj:Det (um) | LatRez (um)
LASER | 1.12 | 2464 | 30000 | 0.405 | 6084 | 0.89
SFSU | 1.12 | 2464 | 30000 | 0.405 | 6084 | 0.89
LED | 1.12 | 2464 | 30000 | 0.43 | 5799 | 0.90
SFSU | 1.12 | 1944 | 30000 | 0.65 | 3335 | 1.00
SFSU | 1.4 | 1944 | 30000 | 0.405 | 7162 | 1.07
SFSU | 1.4 | 1944 | 30000 | 0.65 | 4904 | 1.17
LASER
SF-AW210 405um laser collimated and focused
2 aspheric lenses focal length 11mm ($87 each, C220TMD-A, Thorlabs Inc.)
Aingle-mode optical fibre, core dia 3 μm ($99, S405-XP, Nufern Inc.)
Glass plate, at z = 5.91 mm, beam diameter of 3.8 mm
LED
3 W High Power LED 430 nm–435 nm ($3)
Pinhole 15 μm ($75, P15D, Thorlabs Inc.)
The pictures are acquired with a fixed white balance.

## Slide 9: Holograms at times t1, t2, t3… h1, h2, h3 …
Sum as (h1-h2) + (h3-h4)+…..
Do reconstruction on one summed image
(may need to scale so not to saturate pixels)

## Slide 10
Capture sequence of holograms (h1, h2, h3) at times t1, t2, t3
Sum as (h1-h2) + (h3-h4)+ …..
Do reconstruction on one summed image
(may need to scale so not to saturate pixels)
Encoding x,y,z,t in one Hologram